## Slide 1: Computer Organization and Architecture
A TOP-LEVEL VIEW OF COMPUTER FUNCTION AND INTERCONNECTION
Dr John O’Donoghue

## Slide 2: Topics
Computer Components
Computer Function
Interconnection Structures
Bus Interconnection
PC Buses

## Slide 3: Computer Components
Three key concepts of von Neumann Architecture
  Data and instructions are stored in a single R/W memory
  Contents of memory are addressable by location, without regard to the type of data contained there
  Execution occurs in a sequential fashion (unless explicitly modified), from one execution to the next.
Basic overview of the von Neumann Architecture
  www.computerscience.gcse.guru/theory/von-neumann-architecture
  http://cybercomputing.blogspot.ie/2012/02/von-neumann-architecture.html

## Slide 4: John von Neumann

## Slide 5: Program Concept (1)
Hardware programming
  Customized hardware for a particular computation
  Rewiring hardware for new program
  Hardwired systems are inflexible
General purpose hardware can do different tasks, given correct control signals
  Instead of re-wiring, supply a new set of control signals

## Slide 6: Program Concept (2)
Software programming
  General-purpose configuration of arithmetic and logic function
  What is a program?
    A sequence of steps
    For each step, an arithmetic or logical operation is done
    For each operation, a different set of control signals is needed and applied to the hardware
  Instruction codes  control signals
  New program  New instruction codes

## Slide 7: System Components (1)
CPU
  Instruction interpreter
  General-purpose arithmetic and logic
  functions module
Memory
  Temporary storage of code and results
I/O modules
  Data and instructions need to get into
  the system and results out

## Slide 8: System Components (2)
CPU
  Control Unit: hardware segment accepts codes and issues control signals
  Arithmetic and Logic Unit
  CPU registers
    PC (program counter): address of next instruction to execute
    IR (instruction register): current instruction being executed
    MAR (memory address register): address in memory for next R/W => Load/Store
    MBR (memory buffer register): data to be written/read to/from memory
    I/O AR: particular I/O device
    I/O BR: data exchanged between CPU and I/O module

## Slide 9: System Components (3)
Memory
  A set of locations defined by sequentially numbered addresses
I/O Module
  Contains buffers for temporarily holding data to be exchanged with memory and CPU

## Slide 10: Computer Components: Top Level View

## Slide 11: Computer Function
Basic function?
  Program execution
Program?
  A set of instructions

## Slide 12: Instruction Cycle
Two steps:
  Fetch: CPU reads instructions from memory
  Execute
Instruction cycle = fetch cycle + execution cycle

## Slide 13: Fetch Cycle
How do we know which instruction is next to fetch (i.e. where can we find it)?
  Program Counter (PC or Instruction Pointer IP) holds address of next instruction to fetch
  Processor fetches instruction from memory location pointed to by PC
  Increment PC (to next address in memory, unless told otherwise
Where is the fetched instruction stored?
  Instruction Register (IR)
Processor interprets instruction and performs required actions

## Slide 14: Execute Cycle
Processor-memory
  data transfer between CPU and main memory
Processor I/O
  Data transfer between CPU and I/O module
Data processing
  Some arithmetic or logical operation on data
Control
  Alteration of sequence of operations
  e.g. jump
Combination of above
Animation
www.youtube.com/watch?v=xfJbpCJSpd8

## Slide 15: Example of Program Execution
Characteristics of a
Hypothetical Machine
Load = Read
Store = Write

## Slide 16: Example of Program Execution
Want to perform: Loc941  Loc940 + Loc941
One address format
LOAD 940; AC  Loc940
ADD 941; AC  AC + Loc941
STORE 941; Loc941  AC
Hex representation of instruction
1940 = 0001 1001 0100 0000
e.g. OP-code of LOAD

## Slide 17: Example of Program Execution (Figure 3.5 in the text)

## Slide 18: Instruction Cycle - State Diagram
Fetch = Load = Read

## Slide 19: Instruction Cycle Cont’d

## Slide 20: Interrupts
Mechanism by which other modules (e.g. I/O) may interrupt normal sequence of processing
Program
  e.g. overflow, division by zero
Timer
  Generated by internal processor timer
  Used in pre-emptive multi-tasking
I/O
  from I/O controller, completion of I/O or error
Hardware failure
  e.g. memory parity error, power failure

## Slide 21: Why are Interrupts Useful?
Devices are slow, using an interrupt improves processing efficiency by..
  letting CPU execute its normal instruction sequence and
  pause to service the external devices when they signal that they are ready for CPU’s attention

## Slide 22: Program Flow Control (1)

## Slide 23: Program Timing Short I/O Wait

## Slide 24: Program Timing Long I/O Wait

## Slide 25: Program Flow Control (2)

## Slide 26: Interrupt Cycle
Added to instruction cycle
Processor checks for interrupt
  Indicated by an interrupt signal
If no interrupt, fetch next instruction
If interrupt pending:
  Suspend execution of current program
  Save context
  Set PC to start address of interrupt handler routine
  Process interrupt
  Restore context and continue interrupted program

## Slide 27: Instruction Cycle with Interrupts

## Slide 28: Instruction Cycle (with Interrupts) - State Diagram

## Slide 29: Multiple Interrupts
Disable interrupts - Sequential approach
  Processor will ignore further interrupts whilst processing one interrupt
  Interrupts remain pending and are checked after first interrupt has been processed
  Interrupts handled in sequence as they occur
Define priorities - Nested approach
  Low priority interrupts can be interrupted by higher priority interrupts
  When higher priority interrupt has been processed, processor returns to previous interrupt

## Slide 30: Multiple Interrupts - Sequential

## Slide 31: Multiple Interrupts - Nested

## Slide 32: Time Sequence of Multiple Interrupts

## Slide 33: Interconnection Structures
All the units must be connected
Interconnection structure:
The collection of paths connecting system modules
Different type of connection for different type of unit
  Memory
  Input/Output
  CPU
Design depends on necessary exchanges between modules

## Slide 34: Data Transfer
Memory  CPU
CPU  Memory
I/O  CPU
CPU  I/O
I/O  Memory (?)
DMA: direct memory access

## Slide 35: Computer Modules

## Slide 36: Memory Connection
Receives and sends data
Receives addresses (of locations)
Receives control signals
  Read
  Write
  Timing

## Slide 37: Input/Output Connection(1)
Similar to memory from computer’s viewpoint
Output
  Receive data from computer
  Send data to peripheral
Input
  Receive data from peripheral
  Send data to computer

## Slide 38: Input/Output Connection(2)
Receive control signals from computer
Send control signals to peripherals
  e.g. spin disk
Receive addresses from computer
  e.g. port number to identify peripheral
Send interrupt signals (control)

## Slide 39: CPU Connection
Reads instruction and data
Writes out data (after processing)
Sends control signals to other units
Receives (& acts on) interrupts

## Slide 40: Bus Interconnection (1)
Bus:
  A communication pathway connecting two or more devices
  Characteristics
    Shared
    Usually broadcast
    must ensure only one device transmitting at a time
  Often grouped
    A number of channels in one bus
    e.g. 32 bit data bus is 32 separate single bit channels

## Slide 41: Buses Interconnection (2)
There are a number of possible interconnection systems
Single and multiple BUS structures are most common
  e.g. Control/Address/Data bus (PC)
  e.g. Unibus (DEC-PDP)

## Slide 42: System Bus
Bus that connects major computer components
Typically 50-100 separate lines
Three functional groups of lines
  Data
  Address
  Control
Misc. lines
  power
  ground
  clock

## Slide 43: Data Bus
Carries data
  I.e., moves data between system modules
  Remember that there is no difference between “data” and “instruction” at this level
Width is a key determinant of performance
  Number of lines (1 bit carried by a line at a time)
  Determines number of bits can be transferred at a time
  8, 16, 32, 64 bit

## Slide 44: Address bus
Identify the source or destination of data
  e.g. CPU needs to read an instruction (data) from a given location in memory or an I/O port
Width determines maximum memory capacity of system
  e.g. 8080 has 16 bit address bus giving 64k address space

## Slide 45: Control Bus
Control and timing information
  Memory read/write signal
  Interrupt request
  Clock signals
  access/use of data/address lines

## Slide 46: Bus Interconnection Scheme

## Slide 47: Big and Yellow?
What do buses look like?
  Parallel lines on circuit boards
  Ribbon cables
  Strip connectors on mother boards
    e.g. PCI
  Sets of wires

## Slide 48: Bus Operation
Module wishing to send
  1. Obtain use of bus
  2. Transfer data via bus
Module wishing to receive
  Obtain use of bus
  Transfer request to the other module
  Wait

## Slide 49: Single Bus Problems
Lots of devices on one bus leads to:
  Propagation delays
    Long data paths mean that co-ordination of bus use can adversely affect performance
    If aggregate data transfer approaches bus capacity
    More devices, longer delay
Most systems use multiple buses to overcome these problems
  Hierarchical
  Traditional
  High-performance

## Slide 50: Traditional (ISA) (with cache)

## Slide 51: High Performance Bus

## Slide 52: Elements of Bus Design
Bus type
Bus width
Data transfer type
Arbitration method
Bus timing

## Slide 53: Bus Types
Dedicated
  Separate data & address lines
Multiplexed
  Shared lines
  Address valid or data valid control line
  Advantage - fewer lines
  Disadvantages
    More complex control
    Potential reduction in performance

## Slide 54: Bus Width and Data Transfer Type
Bus width
  Data
  Address
Data transfer type
  Read
  Write
  Read-modify-write: protecting shared memory
  Read-after-write: checking
  Block data transfer

## Slide 55: Bus Arbitration
Why arbitration?
  More than one module controlling the bus, e.g. CPU and DMA controller
  We want to make sure that only one module can successfully transmit over bus at a time
Arbitration may be centralised or distributed

## Slide 56: Centralised Arbitration
Single hardware device controlling bus access
  Bus Controller
  Arbiter
May be part of CPU or separate

## Slide 57: Distributed Arbitration
Each module may claim the bus
Control logic on all modules

## Slide 58: PCI Bus
Peripheral Component Interconnection
Intel released to public domain
32 or 64 bit
49 mandatory and 51 optional signal lines (see Tables 3.3 and 3.4, respectively)
Current standard
  Up to 64 data lines at 66Mhz
  Q: what is the max raw transfer rate?

## Slide 59: Foreground Reading
Stallings, chapter 3
www.pcguide.com/ref/mbsys/buses/