## Slide 1: Whole Body and Hand Vibration Monitoring in Marine settings
Dr Mary Daly Dr Simon Woodworth

## Slide 2: Overview
Irish Naval Service makes extensive use of RHIBs (Rigid Hull Inflatable Boats for:-
  Search And Rescue
  Humanitarian
  Interdiction of trawlers
  Interdiction of drug traffickers
Wave impact on an RHIB travelling at speed can be considerable
  Shock absorbing seats are used.

## Slide 3: Whole Body and Hand Vibration
Medical issues
  Prolonged exposure results in back and neck pain (WBV) and seriously disabling problems with hands wrists and lower arms (HAV).
  Low-frequency motion, from about 5 to 20 Hertz (cycles per second), is thought to be potentially more damaging than higher frequency motion. Vibration at frequencies below 2 Hz and above 1,500 Hz is thought to be less damaging.
Applicable Exposure Standards
  IS02631: Mechanical vibration and shock -Evaluation of human exposure to whole-body vibration
  UK HSE: Controlling vibration risks
  Irish HSA 2007: Control of vibration at work

## Slide 4: Exposure Limits
Hand-Arm Vibration (HAV)
  The daily exposure limit value standardised to an eight-hour reference period shall be 5m/s2;
  The daily exposure action value standardised to an eight-hour reference period shall be 2.5 m/s2.
Whole-body vibration (WBV)
  The daily exposure limit value standardised to an eight-hour reference period shall be 1.15 m/s2
  The daily exposure action value standardised to an eight-hour reference period shall be 0.5 m/s2

## Slide 5: So what’s the problem?
The applicable standards and measurement techniques work well for construction equipment, hand tools and heavy machinery.
Diggers, Kango hammers, Drills, Chainsaws, etc.
The environment in a RHIB is much more variable
Standards are not normalised for marine use

## Slide 6: Investigations so far
Naval Service in conjunction with Dell :-
  Dell identified suitable Ruuvitag sensors for body use and integrated them with an IoT hub to gather data.
  Measurements taken in Cork harbour with a Naval Service RHIB
    Hand
    Belly (kidney nelt)
    Neck
    Hull
The RNLI (Poole, Dorset) has since become involved
  Their concern is impact spike delivering a high G shock

## Slide 7: UCC involvement
Staff and students of the CUBS BIS MSc in Business Information Analytics Systems have been providing analytic support
  Part of relevant modules, in particular Programming for Data Analytics
  Using Anaconda distribution of Python
We have done some initial naïve estimates of g exposure and have normalised to 8-hour exposure standard.
  Efforts have focused on filtering data and understanding context of what is being measured

## Slide 8: Problems and challenges
Can we measure body and hand vibration exposure without having to wire up crew members all the time?
  E.g can we derive exposure from seat and hull sensors?
Ruuvitag sensors have huge battery life and are waterproof but are limited in capability:
  Only 3-axis (accelerometer)
  Cannot easily filter out G due to Earth
  Therefore cannot derive linear acceleration

## Slide 9: Immediate next steps
Upgrade sensors to MetaMotionC / MetamotionR
  More expensive
  Provides 9-axis measurement (Accelerometer, Gyroscope, Magnetometer)
  On-board sensor fusion yields Linear Acceleration
Integrate with Dell IoT Hub
  Bluetooth Beacon
Gather fresh data
  Several bost trips required

## Slide 10: Analytics plan
Gather data
  Frequency filters
  Exposure measures
  Correlation of body, seat and hull measurements
  Log short duration impact spikes
Build models to:
  Deliver % daily exposure measure for given time at sea
  Estimate exposure given hull type (design issue for RNLI)
  Estimate likely impact exposure given hull type and sea conditions